## Slide 1: Thoracic Ultrasound in Context: Pleural Procedure Safety Rahul Bhatnagar Consultant Respiratory Physician / Honorary Senior Lecturer BTS Thoracic Ultrasound Module

## Slide 2: Outline
Recap - Why is thoracic ultrasound important?
Practical applications of respiratory physician delivered thoracic ultrasound
Cautions and limitations

## Slide 3: Improved safety
Section 1

## Slide 4: Real Life Quotes
“Never needed it before”
“Can’t do any harm with a small / green needle”
“I’m a surgeon… I can deal with any problems I might cause!”

## Slide 5
12 deaths
15 serious harm
Seldinger drains
Multiple reports of poor management
Ultrasound guidance strongly recommended
Ask the question: “Can it wait?”

## Slide 6: Retrospective survey of critical incidents associated with chest drain insertion in 101 acute Trusts (2003-2008)
Injury type | Trusts | Number of cases | Deaths | % fatal
Lung or chest wall injury | 35 | 47 | 8 | 17
Wrong side | 5 | 6 | 2 | 33
Lost wire | 3 | 3 | 0 | 0
Inserted into organ /major vessel | 24 | 31 | 7 | 23
Total | 67 | 87 | 17 | 20
Notes: High proportion of fatalities – if it goes wrong, it goes wrong big style

## Slide 7: TUS Evidence - 1
Consecutive patients requiring a diagnostic pleural tap had a proposed site marked by different grades of physicians (CXR and examination)
In total 172/255 (67%) potential sites were proposed
Marked site assessed for accuracy and safety
No relationship between accuracy and experience of doctor
25 were inaccurate (15%), 17 marked sites were over solid organs
Ultrasound identified a site in 54% of the unmarked cases.
Thoracic USS increased yield and reduced risk of solid organ puncture, even in experienced physicians’ hands
Notes: Evidence for USS utility.
Could argue that people do quite well but if things were to go wrong they would have gone wrong badly.
US safer, more accurate

## Slide 8: TUS Evidence - 2
Retrospective cohort over 2 year period
61,261 thoracenteses (45% US-guided)
2.7% pneumothorax rate overall
Ultrasound reduced risk of pneumothorax by 19%
Which in turn reduced costs of hospitalisation
Mercaldi et al. Chest 2013

## Slide 9
Notes: Early referral to chest teams for fluid. US now in guidance

## Slide 10: Uses for Tus - inpatient
Section 2

## Slide 11: Respiratory Ward / Procedure Room
Guidance for all diagnostic and therapeutic aspirations and Seldinger chest drain insertions
Identification of complicated parapneumonic effusions requiring tube drainage/early referral for surgery
Identify presence of pleural effusion when CXR unclear
Confirm drainage complete pre talc pleurodesis
Confirm pleurodesis before chest tube removal
Identification of pneumothorax
Psallidas et al. Lancet Resp Med 2021

## Slide 16
Notes: Loss of sliding sign
Loss of comet tails
Lung point
Need linear probe

## Slide 17: Uses for tus - outpatient
Section 3

## Slide 18: Uses – Outpatients / Procedure list
Clinical assessment / Differential diagnosis
  Fluid characteristics, pleural thickening, diaphragmatic nodularity
Fluid volume assessment -
  Choosing best first pleural procedure
  Identifying need for immediate drainage
Planning later procedures
  Thoracoscopy / IPC placement / IPC removal / US-guided biopsy
Guidance of induced pneumothorax in small effusions
On-table safe site selection for port placement
  16.7% failure with blind approach vs 0% with TUS (P<0.05)
Medford et al. Thorax 2009

## Slide 19: TUS for Diagnosis
Patient with cough and sweats
CRP 152
Pleural fluid pH 6.9

## Slide 22: Cautions
Section 4

## Slide 23: Pleural Effusions
Can be mimicked by / contributed to by
  Collapse
  Consolidation
  Raised hemidiaphragm
  Herniae
  Vascular structures
Additional modes (e.g., Doppler) may be useful

## Slide 25: Bedside Ultrasound

## Slide 26
Notes: Massive aortic aneurysm in safe triangle

## Slide 27: Key Points
All fluid is not pleural fluid!
Seek help with unusual appearances before proceeding
If uncertain – do not proceed

## Slide 28: Intercostal Vessels
Routine assessment only performed in few centres
TUS can identify intercostal vessels, with
  Correct probe
  Practice / experience
  Doppler
  86% sensitivity
Procedure site selection is a compromise
  Between fluid distribution on US and preference for the safe triangle.
Salamonsen et al. Respirology 2013
Notes: Physician-performed ultrasound can accurately screen for a vulnerable intercostal artery prior to chest drainage procedures.
Salamonsen M1, Dobeli K, McGrath D, Readdy C, Ware R, Steinke K, Fielding D.
Author information
Abstract
BACKGROUND AND OBJECTIVE:
Laceration of the intercostal artery during pleural procedures is a rare but serious complication. This study evaluates the utility of thoracic ultrasound (US) to screen for a vulnerable vessel compared with the gold standard computed tomography (CT).
METHODS:
Before undergoing contrast-enhanced CT chest, thoracic US was performed on 50 patients with a high-end and portable machine, and an attempt made to visualize the vessel at three positions across the back to the axilla. These positions were labelled with radio-opaque fiducial markers. On both US and CT images, the location of the vessel at each position, relative to the overlying rib, was calculated and compared.
RESULTS:
The vessel was unshielded by a rib according to CT in 114 of the 133 positions. The sensitivity, specificity and negative predictive value of portable US to image the vessel, when it was within the intercostal space on CT, was 0.86, 0.30 and 0.27 respectively. The performance of a high-end machine was not significantly different. The median time required for a pulmonologist to locate the vessel was 42 s and 18 s for the portable and high-end US respectively.
CONCLUSIONS:
US can be used to screen for a vulnerable vessel prior to pleural procedures, in a time amenable to use in clinical practice. Further, it is achievable by a pulmonologist using a portable US machine. If thoracentesis or chest tube insertion is being performed on a patient at increased risk of bleeding, screening for a vulnerable vessel with US prior to beginning the procedure is recommended.

## Slide 29: Pitfalls in Pneumothorax Identification
Multiple pathologies can impede lung sliding
  Pleural adhesions
  Bullous disease
  Apnoea / Lack of ventilation
  Selective ventilation of single lung
Size / complexity of pneumothorax not easily determined
If in doubt – get alternative imaging

## Slide 30: Summary Points
TUS improves safety and accuracy of pleural procedures
It can supplement a wide variety of clinical scenarios
It should be used routinely with appropriate training
Care needs to be taken with unusual fluid appearances and pneumothorax
Know its limitations and, more importantly, your limitations